## Slide 1: Electronic & Embedded Systems
- Electronic design
& manufacturing
Lecture 04
Brice PARILUSYAN
PhD Student
brice.parilusyan@gmail.com

## Slide 2: Course overview
01|
02|
03|
Tools
PCB technologies
Circuit design

## Slide 3
Tools
Electronic tools
Soldering tools

## Slide 4
1|
Tools
Electronic tools
Multimeter
Oscilloscope
Power supply
Wave generator

## Slide 5
1|
Tools
Definition :
A multimeter is an electronic tool who measure resistance, capacitance, voltage and intensity. Some of them integrate supplementary modules.
Multimeter

## Slide 6
1|
Tools
Definition :
An oscilloscope, or oscillograph, is a measuring instrument designed to display an electrical signal, usually variable over time.
A distinction is generally made between analog oscilloscopes that directly use a multiple of the input voltage to produce the spot deviation and digital oscilloscopes that, prior to any processing, transform the input voltage into a number.
Oscilloscope

## Slide 7
1|
Tools
Definition :
A power supply is an electrical device that supplies electric power to an electric load. The primary function of a power supply is to convert current from a source to the correct voltage, current, and frequency to power the load. As a result, power supplies are sometimes referred to as electric power converter.
Power supply

## Slide 8
1|
Tools
Definition :
A function generator is usually a piece of electronic equipment or software used to generate different types of electrical waveforms over a wide range of frequencies. Some of the most common waveforms produced by the function generator are the sine wave , square wave, triangular wave and sawtooth shapes.
Wave generator

## Slide 9
1|
Tools
Soldering tools
Iron solder
Soldering accessories
SMD soldering

## Slide 10
1|
Tools
Definition :
A soldering station is a multipurpose power soldering device designed for electronic components soldering. This type of equipment is mostly used in electronic and electrical engineering.
Soldering and desoldering use different temperatures. It’s important to understand that too high temperatures lead to a destruction of the device.
Zener diodes

## Slide 11
1|
Properties :
Solder tin have different size and quality. Melting temperature around 230°.
Desoldering bread is used to remove unwanted tin. Better to use it with flux and higher temperature than normal.
Soldering flux reduce oxidation during soldering and improve it. USE A MASK OR AIR CLEANER AROUND, CREATE SMOKE
Soldering accessories
Tools

## Slide 12
1|
Properties :
Reflux oven is used to bake PCB. Depending of the composition of the solder paste used, you must program a specific baking process
Mask is a metallic sheet with holes corresponding with the soldering points of the PCB. It is used to spray correctly soldering paste on the PCB
SMD soldering
Tools

## Slide 13
PCB technologies
THT
SMD

## Slide 14
2|
PCB technologies
THT
Description
Soldering
Desoldering

## Slide 15
2|
Description :
Trough Hole Technology (THT) represent all the electronic components who need to go trough the board to be solder. Most of the component have a THT type, they are the easiest way to make a PCB.
Description
PCB technologies

## Slide 16
2|
Soldering
PCB technologies
Tips :
One of the most important tips is the most simple and difficult, be patient ! Generaly, if it doesn’t work is because one of the part you try to solder didn’t have time to warm up, or because your soldering tool is dirty.

## Slide 17
2|
Tips :
Do not hesitate to use flux and desoldering bread. One of the most important tips is the most simple and difficult, be patient !
Desoldering
PCB technologies

## Slide 18
2|
Tips :
Cleaning the iron solder is extremely important. The oxidation from the heat make it dirty, you need to use solder to clean it. If it doesn’t work, use a sharp tool and scratch it. BE CAUTIOUS, THIS PROCESS DESTROY THE IRON SOLDER.
Cleaning
PCB technologies

## Slide 19
2|
PCB technologies
SMD
Description
Soldering
Desoldering
Cleaning

## Slide 20
2|
Definition :
Surface Mounted Technology (SMD) refer to electronic component who can be solder on one surface of a PCB. Most of the component can be found in this shape, especially integrated circuits (IC). Take care of them, they are fragile.
Description
PCB technologies

## Slide 21
2|
Tips :
SMD have different legs size. Some of them are tedious or impossible to solder with an iron solder. You need to use oven for it. The solder paste use need to have a specific warming cycle to solder properly, take care of the solder you are using.
Soldering
PCB technologies

## Slide 22
2|
Tips :
SMD desoldering isn’t a perfect process. Most of the time, we doesn’t salvage SMD part because their desoldering damage them. If you wish to do it anyway, doesn’t hesitate to use flux and learn to use a, hot air desoldering
Desoldering
PCB technologies

## Slide 23
Circuit design
Integrated circuit (IC)
Manufacturing design

## Slide 24
3|
Digital electronic
Integrated circuit (IC)
History
Manufacturing
Datasheet

## Slide 25
3|
Digital electronic
Definition :
Integrated circuit (IC) is a component who contain a specific circuit inside. It was first demonstrated by Jack Kilby in 1958, then upgraded and developed for massive production in 1959 by Giggle Byte. Each IC is made from silicon, a mineral component who represent a quarter of the earth crust. At middle 1960, an IC contain hundred of transistors. Today, an IC 1x1cm can contain several billion transistors.
History

## Slide 26
3|
Digital electronic
Definition :
Photolithography is a process used in microfabrication, especially for IC. It uses light to transfer a geometric pattern from a photomask to a photosensitive chemical on the substrate. A series of chemical treatments expose the pattern and enables deposition of a new material in the desired pattern upon the material underneath the photoresist. For the more complex IC, wafer may go through the photolithographic cycle as many as 50 times.
Manufacturing

## Slide 27
3|
Digital electronic
Definition :
A datasheet is a document that summarizes the performance and other characteristics of a product, machine, component etc...
In electronic, each IC come with a datasheet. If you have a question about the component, the answer is inside the datasheet.
Datasheet

## Slide 28
3|
Digital electronic
Manufacturing design
Upverter
ATmega328

## Slide 29
3|
Digital electronic
1) Go on internet
2) Go on upverter.com
3) Create an account
4) Let’s make a PCB
Upverter

## Slide 30
3|
Digital electronic
1) Create a circuit with an atmega328, don’t forget the external clock and resistors
2) Add a multiplexer with Leds
3) Add a multiplexer with logic gates to create an external adder 4-bit
4) Don’t forget the connectors and power stage ;)
ATmega328